## Slide 1: ECE 3436 Microprocessor Systems Notes 10a: Special Purpose Registers
Ph.D. Jianfeng Zheng
Dept. ECE, Univ. of Houston
Email: jzheng4@central.uh.edu
Mar 24, 2026
Adapted from notes by Dr. Diana De La Rosa-Pohl

## Slide 2: Today’s agenda in ECE 3436
Describe how the Program Counter (PC) register is used in program execution.
Describe how the Link Register (LR) is used with branches.
Describe how the Stack Pointer (SP) register is used
  Describe how/where the Stack is initialized.
  Describe how the Stack Pointer (SP) works with the Stack memory space.
  PUSH data to the stack
  POP data from the stack

## Slide 3: TM4C123 High-level Block Diagram
We are back

## Slide 4: Memory layout

## Slide 5: Special Purpose Register
32 bit wide
Special Purpose Register
  R13: Stack Pointer (SP)
  R14: Link Register (LR)
  R15: Program Counter (PC)
We are here

## Slide 6: The Program Counter (PC)
Program Counter (PC)
  Current location in the program
  What is “location”
Location

## Slide 7: Encoding (Thumb-2)

## Slide 8: Encoding (Thumb-2)
MOV R1, #1
F
0
4
F
0
1
0 1

## Slide 9: PC in action
Open class demon project
ClassDemo_PC.zip file
OR
Enter the following instructions after the start label in a blank project
MOV R0, #0
MOV R1, #1
MOV R2, #2
ADD R3, R1, R2
B skip
LSL R3, #0x2
skip
LSR R3, #0x1
NOP

## Slide 10: Special Purpose Register
32 bit wide
Special Purpose Register
  R13: Stack Pointer (SP)
  R14: Link Register (LR)
  R15: Program Counter (PC)
We are here

## Slide 11: We already know how to use branch
C Code
varZ = varX + varY
Assembly Code
LDR R1, =varX
LDR R0, [R1]
LDR R1, =vary
LDR R2, [R1]
ADD R0, R0, R2
LDR R1, =varZ
STR R0, [R1]

## Slide 12: Subroutines!
C Code
varZ = sum(varX, vary)
Assembly Code
LDR R1, =varX
LDR R0, [R1]
LDR R1, =vary
LDR R2, [R1]
ADD R0, R0, R2
LDR R1, =varZ
STR R0, [R1]

## Slide 13: The Link Register (LR) In Action
Open class demon project
ClassDemo_LR.zip file
Enter the following instructions after start label

## Slide 14: Branching With Link
BL
  Causes a branch to “label” and copies the address of the instruction into LR
BX
  Branch to an address contained in a register

## Slide 15: Link Register
Holds your spot while you jump to a subroutine

## Slide 16: ROM
28A | 28B | 28C | 28D | 28E | 28F | 290 | 294 | 298
00 | F0 | 02 | F8 | 42 | 1E | 02 | E0 | 
PC
LR
Current instruction
ARM uses bit 0 of LR register to encode execution state
bit[0] = 0 → ARM mode
bit[0] = 1 → Thumb mode

## Slide 17: LR

## Slide 18: LR

## Slide 19: Special Purpose Register
32 bit wide
Special Purpose Register
  R13: Stack Pointer (SP)
  R14: Link Register (LR)
  R15: Program Counter (PC)
We are here

## Slide 20: Reading From RAM
R0 | 
R1 | 
R2 | 
… | …
0x20000000 | AB | CD | EF | 12
0x20000004 | 00 | 00 | 00 | 00
0x20000008 |  |  |  | 
0x2000000C |  |  |  | 
… |  |  |  | 
ARM Processor
Memory
Address bus
Data bus
Control signals
LDR R1, =0x20000000
LDR R0, [R1]
LDR H R0, [R1]
LDR B R0, [R1]

## Slide 21: Write A Byte To RAM
R0 | 
R1 | 
R2 | 
… | …
0x20000000 | AA | CD | EF | 12
0x20000004 | 00 | 00 | 00 | 00
0x20000008 |  |  |  | 
0x2000000C |  |  |  | 
… |  |  |  | 
ARM Processor
Memory
Address bus
Data bus
Control signals
LDR R1, =0x20000000
MOV32 R0, #0xDDCCBBAA
STRB R0, [R1]

## Slide 22: Write A Byte To RAM
R0 | 
R1 | 
R2 | 
… | …
0x20000000 | AA | BB | CC | DD
0x20000004 | 00 | 00 | 00 | 00
0x20000008 |  |  |  | 
0x2000000C |  |  |  | 
… |  |  |  | 
ARM Processor
Memory
Address bus
Data bus
Control signals
LDR R1, =0x20000000
MOV32 R0, #0xDDCCBBAA
STR R0, [R1]

## Slide 23: Memory MAP
Memory
Stack is R/W
  It is in RAM
Starting value of OUR Stack Pointer = 0x20000400
  What is it?
  How to calculate?
Stack Pointer value  R13
256K Flash ROM
32K RAM
I/O ports
Internal I/O
PPB
0x00000000
0x0003FFFF
0x20000000
0x20007FFF
0x40000000
0x400FFFFF
0xE0000000
0xE0041FFF

## Slide 24: Write To Stack  PUSH
R0 | AAAA.AAAA
R1 | BBBB.BBBB
R2 | CCCC.CCCC
… | …
0x200003F0 |  |  |  | 
0x200003F4 |  |  |  | 
0x200003F8 |  |  |  | 
0x200003FC |  |  |  | 
0x20000400 |  |  |  | 
ARM Processor
Memory
Address bus
Data bus
Control signals
;SP = 0x2000.0400 (empty stack)
PUSH {R0} ;SP=0x2000.03FC after PUSH
PUSH {R1} ;SP=0x2000.03F8 after PUSH
PUSH {R1} ;SP=0x2000.03F4 after PUSH

## Slide 25: Write To Stack  PUSH
R0 | AAAA.BBBB
R1 | BBBB.CCCC
R2 | CCCC.DDDD
… | …
0x200003F0 | 00 | 00 | 00 | 00
0x200003F4 | DD | DD | CC | CC
0x200003F8 | CC | CC | BB | BB
0x200003FC | BB | BB | AA | AA
0x20000400 |  |  |  | 
ARM Processor
Memory
Address bus
Data bus
Control signals
;SP = 0x2000.0400 (empty stack)
PUSH {R0} ;SP=0x2000.03FC after PUSH
PUSH {R1} ;SP=0x2000.03F8 after PUSH
PUSH {R2} ;SP=0x2000.03F4 after PUSH

## Slide 26: Read From Stack  POP
R0 | 
R1 | 
R2 | 
… | …
0x200003F0 |  |  |  | 
0x200003F4 | DD | DD | CC | CC
0x200003F8 | CC | CC | BB | BB
0x200003FC | BB | BB | AA | AA
0x20000400 |  |  |  | 
ARM Processor
Memory
Address bus
Data bus
Control signals
;SP = 0x2000.03F4 (current pointer)
POP {R2} ;SP=0x2000.03F8 after POP
POP {R1} ;SP=0x2000.03FC after POP
POP {R0} ;SP=0x2000.0400 after POP

## Slide 27: The Stack FAQ
What is STACK
  Read/Write memory. It is specifically reserved for very short-term data storage
Where is it
  RAM, given it is read/write memory
How is it created?
  Using directives, as configured in the Startup.s file
  EQU, AREA, SPACE, __initial_sp

## Slide 28: The Stack FAQ
How is it used?
  Since you have very few registers, the stack can work as an extension of the register bank. But unlike registers, it is located off of the Microprocessor core (in RAM)
  The stack is used with subroutines to save the state of the register bank so that subroutines can freely use the registers in their calculations.
How do you access the stack?
  Through the PUSH and POP instructions.
Why is the stack so weird
  Last In, First Out
  It stores data backwards.

## Slide 29: The Stack: Before Push
R0 | 0x00112233
R1 | 0x44556677
R2 | 0xAABBCCDD
R3 | 0x12345678
0x200003F0 |  |  |  | 
0x200003F4 |  |  |  | 
0x200003F8 |  |  |  | 
0x200003FC |  |  |  | 
0x20000400 |  |  |  | 
ARM Processor
Memory
; Code PUSH
PUSH {R0}
PUSH {R1}
PUSH {R2}
;SP = 0x2000.0400 at reset
; Code POP
POP {R2}
POP {R1}
POP {R0}

## Slide 30: The Stack: After Push
R0 | 0x00112233
R1 | 0x44556677
R2 | 0xAABBCCDD
R3 | 0x12345678
0x200003F0 |  |  |  | 
0x200003F4 | DD | CC | BB | AA
0x200003F8 | 77 | 66 | 55 | 44
0x200003FC | 33 | 22 | 11 | 00
0x20000400 |  |  |  | 
ARM Processor
Memory
; Code PUSH
PUSH {R0}
PUSH {R1}
PUSH {R2}
;SP = 0x2000.03F4 after PUSH
; Code POP
POP {R2}
POP {R1}
POP {R0}

## Slide 31: The Stack: Before POP
R0 | 
R1 | 
R2 | 
R3 | 0x12345678
0x200003F0 |  |  |  | 
0x200003F4 | DD | CC | BB | AA
0x200003F8 | 77 | 66 | 55 | 44
0x200003FC | 33 | 22 | 11 | 00
0x20000400 |  |  |  | 
ARM Processor
Memory
; Code PUSH
PUSH {R0}
PUSH {R1}
PUSH {R2}
;SP = 0x2000.03F4 before POP
; Code POP
POP {R2}
POP {R1}
POP {R0}

## Slide 32: The Stack: After POP
R0 | 0x00112233
R1 | 0x44556677
R2 | 0xAABBCCDD
R3 | 0x12345678
0x200003F0 |  |  |  | 
0x200003F4 | DD | CC | BB | AA
0x200003F8 | 77 | 66 | 55 | 44
0x200003FC | 33 | 22 | 11 | 00
0x20000400 |  |  |  | 
ARM Processor
Memory
; Code PUSH
PUSH {R0}
PUSH {R1}
PUSH {R2}
;SP = 0x2000.0400 after POP
; Code POP
POP {R2}
POP {R1}
POP {R0}

## Slide 33: The Stack: PUSH/POP Multiple Registers
R0 | 0x00112233
R1 | 0x44556677
R2 | 0xAABBCCDD
R3 | 0x12345678
R4 | 
0x200003F0 |  |  |  | 
0x200003F4 |  |  |  | 
0x200003F8 |  |  |  | 
0x200003FC |  |  |  | 
0x20000400 |  |  |  | 
ARM Processor
Memory
; Code PUSH
PUSH {R0-R1, R3, R2}

## Slide 34: The Stack: PUSH/POP Multiple Registers
R0 | 0x00112233
R1 | 0x44556677
R2 | 0xAABBCCDD
R3 | 0x12345678
R4 | 
0x200003F0 | 33 | 22 | 11 | 00
0x200003F4 | 77 | 66 | 55 | 44
0x200003F8 | DD | CC | BB | AA
0x200003FC | 78 | 56 | 34 | 12
0x20000400 |  |  |  | 
ARM Processor
Memory
; Code
PUSH {R0-R1, R3, R2}
… …
POP {R1, R3, R2, R0}

## Slide 35: The Stack: PUSH/POP Multiple Registers
R0 | 0x00112233
R1 | 0x44556677
R2 | 0xAABBCCDD
R3 | 0x12345678
R4 | 
0x200003F0 | 33 | 22 | 11 | 00
0x200003F4 | 77 | 66 | 55 | 44
0x200003F8 | DD | CC | BB | AA
0x200003FC | 78 | 56 | 34 | 12
0x20000400 |  |  |  | 
ARM Processor
Memory
; Code
PUSH {R0-R1, R3, R2}
… …
POP {R1, R3, R2, R0}

## Slide 36: Stack Pointer (SP) Practice
Open class demon project
ClassDemo_PushPop.zip file