## Slide 1: ECE 3436 Microprocessor Systems Notes 4b: Condition Codes I
Ph.D. Jianfeng Zheng
Dept. ECE, Univ. of Houston
Email: jzheng4@central.uh.edu
Feb 12, 2026
Adapted from notes by Dr. Diana De La Rosa-Pohl

## Slide 2: Today’s agenda in ECE 3436
Review 2’s complement numbers
Predict condition flag values
Observe conditions flags during program execution

## Slide 3: 2’s Complement Review
Two’s complement
  Add one extra sign bit and flip all bits
  Add one
1’s
2’s
1’s
2’s

## Slide 4: Condition Flags
The Program Status Register (PSR) is a 32-bit register.
  Application Program Register, APSR (application level/unprivileged Software)
  Interrupt Program Status Register, IPSR (holds exception number)
  Execution Program Status Register, EPSR (Holds execution state bits)

## Slide 5: Condition Flags
FLAGS
  N, bit[31] Negative condition code flag. If the result is regarded as a two’s complement signed integer, then N==1 if the result is negative and N==0 if it is positive or zero.
  Z, bit[30] Zero condition code flag. Set to 1 if the result of the instruction is zero, and to 0 otherwise.
  C, bit[29] Carry condition code flag. Set to 1 if the instruction results in a carry condition.
  V, bit[28] Overflow condition code flag. Set to 1 if the instruction results in an overflow condition.

## Slide 6: Condition Flags
C flag
  Set (1) after an unsigned addition if the answer is wrong
  Clear (0) after an unsigned subtraction if the answer is wrong
V flag
  Set (1) after a signed addition or subtraction if the answer is wrong
Bit | Name | Meaning if set (1)
N | negative | Result is negative
Z | zero | Result is zero
V | overflow | Signed overflow
C | carry | Unsigned addition overflow
T | Thumb mode | Microprocessor is in Thumb mode

## Slide 7: Arithmetic gone wrong
Carry flag warnings
Carry bit SET
  Unsigned addition  Wrong
Carry bit CLEAR
  Unsigned subtraction  Wrong
Overflow flag warnings
Overflow bit SET
  Signed addition  Wrong
  Signed subtraction  Wrong
For SUBS R0, R1, R2, it almost equals to ADDS R0, R1, “R2”
Multiply does not affect the C or V flags, only N&Z
Division does not set flags

## Slide 8: C flag and V flag
Define:
Co: Carry out at MSB (C1)
Ci: Carry in at MSB (C2)
Then:
C = Co
V = XOR (Ci, Co)

## Slide 9: C flag and V flag
Define:
Co: Carry out at MSB
Ci: Carry in at MSB
Then:
C = Co
V = XOR (Ci, Co)
0 1 0 0 0 0 0 1
+ 1 1 0 1 0 0 1 1
1 0 0 0 1 0 1 0 0
Ci, carry in
Co, carry out
In the shown example, Ci = 1, Co =1, we get C = 1 and V = 0.

## Slide 10: C flag and V flag (Arithmetic Logic Unit)
Check the corner case
  MOV R1, #0
  MOV R2, #0
  SUBS R0, R1, R2
For SUBS R0, R1, R2, it almost equals to ADDS R0, R1, “R2”
For “”, we need “Flip” and “+1”
The “+1” is operated during add, not before add.

## Slide 11: How do you know if flags will be updated
Check the FLAGs in debug mode, and
ARM®v7-M Architecture Reference Manual
Cortex-M4 Technical Reference Manual

## Slide 12: EX. 1: Zero (Z) Flag
Ex: 0x10 + 0x01
Answer: ________
Is the answer zero?
  No  Z = 0
  Yes  Z = 1

## Slide 13: EX. 2: Zero (Z) Flag
Ex: 0x00 + 0x00
Answer: ________
Is the answer zero?
  No  Z = 0
  Yes  Z = 1

## Slide 14: Check
0xA0A0.A0A0 + 0x0505.0505
Is the answer zero?
  Z = 0 or 1
Is the answer negative?
Does the calculations produce a carry?
Is the answer correct?
0xFFFF.FFFF + 0x0000.0001
Is the answer zero?
  Z = 0 or 1
Is the answer negative?
Does the calculations produce a carry?
Is the answer correct?

## Slide 15: EX. 3: Negative (N) Flag
Ex: 0x01 + 0x01
Answer: ________
Is the answer negative? How do you know?
  No  N = 0
  Yes  N = 1

## Slide 16: EX. 4: Negative (N) Flag
Ex: 0x0000.0000 + 0xFFFF.FFFF
Answer: ________
Is the answer negative?
  No  N = 0
  Yes  N = 1

## Slide 17: Check
0x1234.ABCD  0x1234.0000
Is the answer negative
  Z = 0 or 1
Is the answer zero?
Does the calculations produce a carry?
Is the answer correct?
0xFFFF.FFFF  0xF000.0001
Is the answer negative?
  N = 0 or 1
Is the answer zero?
Does the calculations produce a carry?
Is the answer correct?

## Slide 18: EX. 5: Carry (C) & Overflow (V) Flags
Ex: 0x0000.0010 + 0x0000.0001
Answer: ________
Unsigned Numbers:
16 + 1 = 7
The answer is correct/incorrect?
Signed Numbers:
16 + 1 = 7
The answer is correct/incorrect?

## Slide 19: EX. 6: Carry (C) & Overflow (V) Flags
Ex: 0x8000.0000 + 0x0000.0001
Answer: ________
Unsigned Numbers:
2,147,483,648 + 1 = 2,147,483,649
The answer is correct/incorrect?
Signed Numbers:
2,147,483,648 + 1 =  2,147,483,647
The answer is correct/incorrect?

## Slide 20: EX. 7: Carry (C) & Overflow (V) Flags
Ex: 0xFFFF.FFFF + 0x0000.0001
Answer: ________
Unsigned Numbers:
4,294,967,295 + 1 =0
The answer is correct/incorrect?
Signed Numbers:
1 + 1 = 0
The answer is correct/incorrect?

## Slide 21: EX. 8: Carry (C) & Overflow (V) Flags
Ex: 0x7FFF.FFFF + 0x7FFF.FFFF
Answer: ________
Unsigned Numbers:
2,147,483,647 + 2,147,483,647 = 4,294,967,294
The answer is correct/incorrect?
Signed Numbers:
2,147,483,647 + 2,147,483,647 =
2
The answer is correct/incorrect?

## Slide 22: EX. 9: Carry (C) & Overflow (V) Flags
Ex: 0x8000.0000 + 0x8000.0000
Answer: ________
Unsigned Numbers:
2,147,483,648 + 2,147,483,648 = 0
The answer is correct/incorrect?
Signed Numbers:
 2,147,483,647 +  2,147,483,647 = 0
The answer is correct/incorrect?

## Slide 23: Now You Try
0x000.0001 + 0x0000.0001
Is the answer zero?
  Z = 0 or 1
Is the answer negative?
  N = 0 or 1
Is there a carry
  C = 0 or 1
Is the answer correct
  V = 0 or 1
0x0000.0001  0x0000.0001
Is the answer zero?
  Z = 0 or 1
Is the answer negative?
  N = 0 or 1
Is there a carry
  C = 0 or 1
Is the answer correct
  V = 0 or 1

## Slide 24: Now You Try
0x6666.6666 / 0x0000.0002
Is the answer zero?
  Z = 0 or 1
Is the answer negative?
  N = 0 or 1
Is there a carry
  C = 0 or 1
Is the answer correct
  V = 0 or 1
0x8000.0000 * 0x0000.0002
Is the answer zero?
  Z = 0 or 1
Is the answer negative?
  N = 0 or 1
Is there a carry
  C = 0 or 1
Is the answer correct
  V = 0 or 1