## Slide 1: ECE 3436 Microprocessor Systems Notes 5a: Shift, Rotate, & Logical Operations
Ph.D. Jianfeng Zheng
Dept. ECE, Univ. of Houston
Email: jzheng4@central.uh.edu
Feb 17, 2026
Adapted from notes by Dr. Diana De La Rosa-Pohl

## Slide 2: Today’s agenda in ECE 3436
Review N, Z, C, and V condition flags.
Perform shift operations on register data
Perform rotate operations on register data
Perform logical operations on register data

## Slide 3: Shift instructions
B7 | B6 | B5 | B4 | B3 | B2 | B1 | B0
1 | 0 | 1 | 1 | 0 | 0 | 1 | 0
R1
LSL – logical shift left
LSR – logical shift right
ASR – arithmetic shift right
LSL R0, R1, #3
  Ans  1001.0000
LSR R0, R1, #2
  Ans  0010.1100
ASR R0, R1, #4
  Ans  1111.1011
8-bit example

## Slide 4: Shift instructions
B7 | B6 | B5 | B4 | B3 | B2 | B1 | B0
0 | 0 | 1 | 1 | 0 | 0 | 1 | 0
R1
What is the result in R0
ASR R0, R1, #3
  Ans  0000.0110 or
  Ans  1110.0110
8-bit example

## Slide 5: Shift instructions
R1 = 1100.1001.0000.0001.0011.0010.0001.1001
What is the result in R0
ASR R0, R1, #3
  Ans  1111.1001.0010.0000.0010.0110.0100.0011
32-bit example

## Slide 6: Shift Multiplication (LSL)
Logical Shift Left
  Multiply by 2 (for each shift)
  Multiply by powers of 2 only
  EX.: LSL R1, R0, #2
0 | 0 | 0 | 1 | 0 | 0 | 1 | 0
0 | 1 | 0 | 0 | 1 | 0 | 0 | 0

31 | 30 | 29 | 28 | 27 | 26 |  |  |  | 1 | 0
C
0n31
Logical Shift Left
LSL
0

## Slide 7: Shift Multiplication (LSL)
4-bit Practice (single shift to left)
0 | 1 | 0 | 0
0 | 0 | 1 | 1
0 | 1 | 1 | 0
1 | 1 | 1 | 1
#1
#2
#3
#4
+4
+6
+3
+15 or 1

## Slide 8: Shift Multiplication (LSL)
8-bit Practice (single shift to left)
0 | 1 | 0 | 0 | 0 | 0 | 0 | 0
#1
+64
0 | 0 | 0 | 1 | 0 | 0 | 0 | 1
#2
+17
1 | 0 | 0 | 0 | 0 | 0 | 0 | 0
#3
+128 or 128
1 | 1 | 1 | 1 | 1 | 1 | 1 | 1
#4
+255 or 1

## Slide 9: Unsigned Shift Division (LSR)
Logical Shift Right
  Divide by 2 (for each shift)
  Divide by powers of 2 only
  EX.: LSR R1, R0, #2
0 | 0 | 0 | 1 | 0 | 0 | 1 | 0
0 | 0 | 0 | 0 | 0 | 0 | 1 | 0

31 | 30 | 29 | 28 | 27 | 26 |  |  |  | 1 | 0
C
1n32
Logical Shift Right
LSR
0

## Slide 10: Unsigned Shift Division (LSR)
4-bit Practice (single shift to right)
1 | 0 | 0 | 0
0 | 0 | 1 | 1
0 | 1 | 1 | 0
0 | 1 | 1 | 1
#1
#2
#3
#4
+4
+6
+3
+7

## Slide 11: Unsigned Shift Division (LSR)
8-bit Practice (single shift to right)
1 | 0 | 0 | 0 | 1 | 0 | 0 | 0
#1
+136
0 | 1 | 1 | 0 | 0 | 1 | 1 | 0
#2
+102
1 | 0 | 0 | 0 | 0 | 0 | 0 | 0
#3
+128 or 128
1 | 1 | 1 | 1 | 1 | 1 | 1 | 1
#4
+255 or 1

## Slide 12: Signed Shift Division (ASR)
Arithmetic Shift Right
  Divide by 2 (for each shift)
  Divide by powers of 2 only
  EX.: ASR R1, R0, #1
1 | 0 | 0 | 1 | 0 | 0 | 1 | 0
1 | 1 | 0 | 0 | 1 | 0 | 0 | 1

31 | 30 | 29 | 28 | 27 | 26 |  |  |  | 1 | 0
C
1n32
Arithmetic Shift Right
ASR

## Slide 13: Signed Shift Division (ASR)
4-bit Two’s Complement Practice (single shift to right)
1 | 0 | 0 | 0
1 | 1 | 0 | 1
0 | 0 | 1 | 0
1 | 0 | 0 | 1
#1
#2
#3
#4
8
?
3
7

## Slide 14: Signed Shift Division (ASR)
8-bit Practice (single shift to right)
1 | 0 | 0 | 0 | 1 | 0 | 0 | 0
#1
120
0 | 1 | 1 | 0 | 0 | 1 | 1 | 0
#2
+102
1 | 0 | 0 | 0 | 0 | 0 | 0 | 0
#3
128
1 | 1 | 1 | 1 | 1 | 1 | 1 | 1
#4
1

## Slide 15: Shift Operations w/carry bit
31 | 30 | 29 | 28 | 27 | 26 |  |  |  | 1 | 0
C
1n32
Logical Shift Right
LSR
0
31 | 30 | 29 | 28 | 27 | 26 |  |  |  | 1 | 0
C
1n32
Arithmetic Shift Right
ASR
31 | 30 | 29 | 28 | 27 | 26 |  |  |  | 1 | 0
C
0n31
Logical Shift Left
LSL
0
Use the ASR instruction when manipulating signed numbers, and use the LSR instruction when shifting unsigned numbers.

## Slide 16: Rotate operations
B7 | B6 | B5 | B4 | B3 | B2 | B1 | B0
1 | 0 | 1 | 1 | 0 | 0 | 1 | 0
R1
ROR – rotate right
RRX – rotate right w/extend
ROR R0, R1, #1
  Ans  ??
RRX R0, R1
  Ans  ??
8-bit example

## Slide 17: Rotate Operations
31 | 30 | 29 | 28 | 27 | 26 |  |  |  | 1 | 0
C
1n32
Rotate Shift Right
ROR
31 | 30 | 29 | 28 | 27 | 26 |  |  |  | 1 | 0
C
0n31
Rotate Right Extended
RRX

## Slide 18: Inverter (Not) Truth Table
Assembly Instructions
MVN{S} Rd, <op2> ;Rd=~op2
Symbol
In | Out
1 | 0
0 | 1
And Truth Table
Assembly Instructions
AND{S} {Rd,} Rn, <op2> ;Rd=Rn&op2
Symbol
In_A | In_B | Out
0 | 0 | 0
1 | 0 | 0
0 | 1 | 0
1 | 1 | 1

## Slide 19: OR Truth Table
Exclusive OR (XOR) Truth Table
Assembly Instructions
EOR{S} {Rd,} Rn, <op2> ;Rd=Rn^op2
Symbol
In_A | In_B | Out
0 | 0 | 0
1 | 0 | 1
0 | 1 | 1
1 | 1 | 0
Assembly Instructions
ORR{S} {Rd,} Rn, <op2> ;Rd=Rn|op2
Symbol
In_A | In_B | Out
0 | 0 | 0
1 | 0 | 1
0 | 1 | 1
1 | 1 | 1

## Slide 20: BIT Clear Truth Table
Assembly Instructions
BIC{S} {Rd,} Rn, <op2> ;Rd=Rn&(~op2)
Symbol
In_A | In_B | Out
0 | 0 | 0
1 | 0 | 1
0 | 1 | 0
1 | 1 | 0
Assembly Instructions
ORN{S} {Rd,} Rn, <op2> ;Rd=Rn|(~op2)
Symbol
In_A | In_B | Out
0 | 0 | 1
1 | 0 | 1
0 | 1 | 0
1 | 1 | 1
OR NOT Truth Table

## Slide 21: Quick Quiz
How do you …?
  SET specific bits (to True) in a register
    2 Ways
  CLEAR specific bits (to False) in a register
    2 Ways
  Toggle (flip) bits in a register
    2 Ways

## Slide 22: PRACTICE
Logical operations without setting flags
  AND R4, R1, #0xFF
  AND R5, R2, R3
  ORR R6, R3, R0
  EOR R7, R3, R0
  BIC R8, R2, R3
  ORN R9, R3, R1
Register | Value
R0 | 0000…0101 1100
R1 | 0000…1101 1001
R2 | 0000…0111 0111
R3 | 0000…1111 0000
R4 | 
R5 | 
R6 | 
R7 | 
R8 | 
R9 | 

## Slide 23: Logical Operations Recap
Logical operations
  AND{S} {Rd,} Rn, <op2> ;Rd=Rn&op2, Clear bits where B=0
  ORR{S} {Rd,} Rn, <op2> ;Rd=Rn|op2, Set bits where B=1
  EOR{S} {Rd,} Rn, <op2> ;Rd=Rn^op2, Toggle bits where B=1
  BIC{S} {Rd,} Rn, <op2> ;Rd=Rn&(~op2), Clear bits where B=1
  ORN{S} {Rd,} Rn, <op2> ;Rd=Rn|(~op2), Set bits where B=0
A Rn | B Operand2 (Mask) | A&B AND | A¦B ORR | A^B EOR | A&(~B) BIC | A¦(~B) ORN
0 | 0 | 0 | 0 | 0 | 0 | 1
0 | 1 | 0 | 1 | 1 | 0 | 0
1 | 0 | 0 | 1 | 1 | 1 | 1
1 | 1 | 1 | 1 | 0 | 0 | 1