## Slide 1: ECE 3436 Microprocessor Systems Notes 6c: Data Storage -- RAM & ROM
Ph.D. Jianfeng Zheng
Dept. ECE, Univ. of Houston
Email: jzheng4@central.uh.edu
Feb 21, 2026
Adapted from notes by Dr. Diana De La Rosa-Pohl

## Slide 2: Today’s agenda in ECE 3436
Create constants in ROM
Create variables in RAM
Read constant values from ROM
Write variable values in RAM
Read variable values in RAM

## Slide 3: Defining/Creating Variables – SRAM
We are here

## Slide 4: RAM Memory Access
Micro
Processor
RAM
(Variables)
Address (32 bits)
Data (32 bits)
System bus
0x2000.0000  0x2000.7FFF
(32 K)

## Slide 5: Defining (Uninitialized) Variables
C data types
  int AGE;
  Char AGET[7];
Assembly SPACE directive
  AGE SPACE 4
  AGET SPACE 7
Create a space in SRAM memory to hold the value of AGE and AGET
Value can be changed when running the program

## Slide 6: In-class Activity 0
Create an AREA in memory (RAM) for your variables
  Use the AREA directive
  Give the area a name
  Make it an area for DATA (as opposed to code)
  Set it up to be READWRITE
  Align the area in RAM to start on a memory address that is a multiple of 4

## Slide 7: In-class Activity 0
  Create the variables to the right
  Use the SPACE directive
  Place directive in DATA AREA of file
  Global variables are permanent at a fixed location in RAM
  Exist for the life of the program
  VARA SPACE 4
  VARB SPACE 2
  VARC SPACE 1
  …

## Slide 8: Storing Values in Variables – Loading an address
LDR Pseudocode version
  LDR Rd, =variable_name
  LDR R0, =VARA
  LDR R1, =VARB
  LDR R2, =VARC
  LDR R3, =otherVarName
  …

## Slide 9: Storing Values in Variables – Storing to an address
Using the STR instruction
  STR Rs, [Ra]
  STR R1, [R2]
    go to the memory address that is stored in R2
    Store the 32 bits in R1 at that address
  STR R3, [R5]
    go to the memory address that is stored in R5
    Store the 32 bits in R3 at that address
Store the value in Rs into the bytes at the memory location in Ra.

## Slide 10: In-class Activity 1A
Storing data into RAM from a register
  Step 0
    Load a register with the value 1
  Step 1
    Load the address of the constant or variable into a register
    Ex: LDR R1,=VARA
    R1 now contains the memory address of VARA
  Step 2
    Store the value in a register to a variable in RAM
    Ex: STR R0, [R1]
    VARA now has the value in R0

## Slide 11: In-class Activity 1B
Storing data into RAM from a register
  Now give the variables VARB and VARC the values 0x1234 and 0xAB
    VARB = 0x1234;
    VARC = 0xAB;
  Pay attention to the size of the variable
  Check values in memory window
To store value to a 16-bit variable
   STRH
To store a value to an 8-bit variable
  STRB

## Slide 12: Loading A Variable Value From RAM
Step 1.
  Load the address of the variable into a register
  Ex: LDR R1, =VARA
  R1 now contains the memory address of VARA
Step 2.
  Load another register with the value stored at that address
  Ex: LDR R3, [R1]
  R3 now has the value in VARA

## Slide 13: In-class Activity 1C
  Load the values from the variables VARB and VARC into register R6 & R7
    VARB  R6
    VARC  R7
  Pay attention to the size of the variable
  Check values in memory window
To store value to a 16-bit variable
   LDRH
To store a value to an 8-bit variable
  LDRB

## Slide 14: Defining/Creating Constants – EEPROM (FLASH)
We are here

## Slide 15: ROM Memory Access
Micro
Processor
ROM
Address (32 bits)
Data (32 bits)
Dcode bus
0x0000.0000  0x0003.fFFF
(256 K)
(Program)
(Constants)
Address (32 bits)
Data (32 bits)
Icode bus

## Slide 16: Defining Constants
C const keyword
  const int AGE=30;
  const char AGET[]=“thirty”;
Assembly DC_ directive
  AGE DCD 30
  AGET DCB “thirty”,0
Create a space in ROM to hold the value of AGE while also initializing the value
Value cannot be changed when running the program

## Slide 17: Defining Constant Data Sizes
Bits
Bytes B  8 bits
Half words W  16 bits
Words D  32 bits
DCB
Define constant byte
8 bits, 1 byte
Aligned on 1-byte boundary
Mybyte DCB 0x23
DCW
Define constant [Half] word
16 bits, 2 byte
Aligned on 2-byte boundary
Myhword DCW 0x584A
DCD
Define constant double (=word)
32 bits, 4 byte
Aligned on 4-byte boundary
Mydouble DCD 0xABCDEF10

## Slide 18: Defining Constant: Strings
Each character in the string is 1-byte (ASCII)
Must manually terminate the string with the null character (0)
Mystr DCB “Hello world!”,0

## Slide 19: Loading A Value
SYNTAX
  LDR Rd, [Ra]
  Load Rd with the contents of the memory address stored in Ra
Examples
LDR R1, [R2]
  Go to the memory address that is stored in R2
  get the 32 bits stored there and load them into R1
LDR R3, [R5]
  Go to the memory address that is stored in R5
  get the 32 bits stored there and load them into R3

## Slide 20: Loading A Constant Value From ROM
Step 1
  Load the address of the constant or variable into a register
  Ex: LDR R1, =VARA
  R1 now contains the memory address of VARA
Step 2
  Load another register with the value stored at that address
  LDR R0, [R1]
  R0 now has the value in VARA

## Slide 21: Loading A Constant Value From ROM
Step 1
  Load the address of the constant or variable into a register
  Ex: LDR R1, =VARA
  R1 now contains the memory address of VARA
Step 2
  Load another register with the value stored at that address
  LDR R0, [R1]
  R0 now has the value in VARA

## Slide 22: Reading/Writing Different DATA Sizes
Load (Memory  Register)
  LDRB unsigned byte
  LDRH unsigned halfword
  LDR word
  LDRD double (into 2 reg.s)
  LDRSH sign extend halfword
  LDRSB sign extend byte
Store (Register  Memory)
  STRB store byte
  STRH store halfword
  STR store word

## Slide 23: Reading/Writing Different DATA Sizes
Load (Memory  Register)
  LDRB unsigned byte
  LDRH unsigned halfword
  LDR word
  LDRD double (into 2 reg.s)
  LDRSH sign extend halfword
  LDRSB sign extend byte
Store (Register  Memory)
  STRB store byte
  STRH store halfword
  STR store word

## Slide 24: In-class activity 2: Parallel Circuit
Given: (Constant)
  Vs = 5V (8 bits)
  R1 = 50 ohm (16 bits)
  R2 = 200 ohm (16 bits)
Solve for: (Variable)
  Req = ?? Ohm (16 bits)
  Is = ?? mA (32 bits)
Write the code to solve for Req & Is