## Slide 1: ECE 3436 Microprocessor Systems Notes 6a: Conditional Branching and Execution
Ph.D. Jianfeng Zheng
Dept. ECE, Univ. of Houston
Email: jzheng4@central.uh.edu
Feb 26, 2026
Adapted from notes by Dr. Diana De La Rosa-Pohl

## Slide 2: Today’s agenda in ECE 3436
Exam #2 will be on Mar 12, Thursday
  Exam #2 Review on Mar 10, Tuesday
Next week will be lab and quiz week
  Mar 3, Tuesday, Quiz 5 on RAM and ROM, Lab #3 on RAM/ROM
  Mar 5, Thursday, Quiz 6 on Conditional branching and execution, Lab #2 on ASCII
Homework 5 and 6 will be published today thru Canvas.
Examples of Quiz 5, 6 and Exam #2 will be shared thru Teams

## Slide 3: Today’s agenda in ECE 3436
Conditional Branching
  Execute an unconditional branch instruction
  Execute branch instructions based on status of the condition flags
Conditional Execution
  Execute instructions based on status of the condition flags

## Slide 4: Unconditional Branch (the B instruction)
Jumps to a label
  No questions asked
Example
Top
MOV R1, #1
B Bottom
MOV R1, #2 ;this will not execute
NOP
Bottom
MOV R1, #3

## Slide 5: Conditional Branch
C Code
if (x==10)
{
y=y+1;}
x = 2;
Assembly Language
LDR R1, =VARX
LDR R0, [R1] ; xR0
;; add code
Addition
LDR R3, =VARY
LDR R2, [R3] ; yR2
ADD R2, #1 ; y=y+1
STR R2, [R3]
NEXT
MOV R0, #2
STR R0, [R1]
How to control Branching?

## Slide 6: General form of the B instruction
SYNTAX
B{cond} label
Branching W/ the Z flag: BEQ and BNE
Branching W/ the C flag: BCS and BCC
Branching W/ the N flag: BMI and BPL
Branching W/ the V flag: BVS and BVC

## Slide 7: More condition code suffixes
Unsigned
BHI Branch if higher
BHS Branch if higher or same
BLO Branch if lower
BLS Branch if lower or same
Signed
BGE Branch if signed greater than or equal
BGT Branch if signed greater than
BLE Branch if signed less than or equal
BLT Branch if signed less than

## Slide 8: Condition Field (Conditional Code)
Mnemonic | Description (for CMP or SUBS) | FLAGS
EQ | Equal | Z==1
NE | Not equal | Z==0
CS/HS | Carry Set/Unsigned higher or same | C==1
CC/LO | Carry Clear/Unsigned lower | C==0
MI | Negative (Minus) | N==1
PL | Positive or zero | N==0
VS | Overflow | V==1
VC | No overflow | V==0
HI | Unsigned higher | (C==1)&&(Z==0)
LS | Unsigned lower or same | (C==0)¦¦(Z==1)
GE | Signed greater than or equal | N==V
LT | Signed less than | N!=V

## Slide 9: Condition Field (Conditional Code)
Mnemonic | Description (for CMP or SUBS) | FLAGS
GT | Signed greater than | (Z==0)&&(N==V)
LE | Signed less than or equal | (Z==1)¦¦(N!=V)
AL | Carry Set/Unsigned higher or same | None tested

## Slide 10: Example
C Code
if (x==10)
{
y=y+1;}
x = 2;
Assembly Language
LDR R1, =VARX
LDR R0, [R1] ; xR0
CMP R0, #10 ; R0-10
BEQ Addition ; z==1
B NEXT ; z!=1
Addition
LDR R3, =VARY
LDR R2, [R3] ; yR2
ADD R2, #1 ; y=y+1
STR R2, [R3]
NEXT
MOV R0, #2
STR R0, [R1]
Do NOT forget !

## Slide 11: Conditional Instruction (Conditional Execution)
Flexible Second Operand (Operand2) can be a:
Constant
Register with optional shift
MOV SYNTAX
MOV{S}{cond} Rd, Operand2
where
S
is an optional suffix. If S is specified, the condition flags are updated on the result of the operation
Cond
is an optional condition code
Rd
is the destination register
Operand2
is a flexible second operand
EX:
MOVEQ R1, #0x1234

## Slide 12: Condition Field (Conditional Code)
Mnemonic | Description (for CMP or SUBS) | FLAGS
EQ | Equal | Z==1
NE | Not equal | Z==0
CS/HS | Carry Set/Unsigned higher or same | C==1
CC/LO | Carry Clear/Unsigned lower | C==0
MI | Negative (Minus) | N==1
PL | Positive or zero | N==0
VS | Overflow | V==1
VC | No overflow | V==0
HI | Unsigned higher | (C==1)&&(Z==0)
LS | Unsigned lower or same | (C==0)¦¦(Z==1)
GE | Signed greater than or equal | N==V
LT | Signed less than | N!=V

## Slide 13: Condition Field (Conditional Code)
Mnemonic | Description (for CMP or SUBS) | FLAGS
GT | Signed greater than | (Z==0)&&(N==V)
LE | Signed less than or equal | (Z==1)¦¦(N!=V)
AL | Carry Set/Unsigned higher or same | None tested

## Slide 14: Try it
Assume that an instruction was just executed that set the flags …
  1. Add 2 to R3 if the result was zero.
  2. Move the value 0 into R0 if the result was NOT zero.
  3. Subtract 5 from R6 if the result was negative.
  4. Multiply R3 times R1 if the previous result caused a carry.

## Slide 15: Example
C Code
if (x==10)
{
y=5;}
Assembly Language
LDR R1, =VARX
LDR R0, [R1] ; xR0
CMP R0, #10 ; R0-10
MOVEQ R2, #5 ; R2=5
LDREQ R1, =VARY
STREQ R2, [R1]

## Slide 16: Example
C Code
if (x<y)
{
x=x+3;}
Assembly Language
LDR R1, =VARX
LDR R2, [R1] ; xR2
LDR R3, =VARY
LDR R4, [R3] ; yR2
CMP R2, R4 ;R2-R4
ADDLT R2, R2, #3
STRLT R2, [R1]